## Slide 1: EG6 – SEISMIC DESIGN
EG6 impacts on both EC7 and EC8
EG6 needs to give his contribution to:
  TC250/SC7 PT2 and PT3 (with a special emphasis on site investigation)
  TC250/SC8 to the PT’s primarely for part 5 and part 1

## Slide 2
:
THE FOLLOWING SUGGESTIONS ARE CONSIDERED FOR POSSIBLE IMPLEMENTATION IN EN 1997:
Clauses 2.1 Design requirements
The pseudo static calculation model should be included in the verification procedures by partial factors.
The complete set of partial factors (model, actions, material or resistances) should be presented in appropriate tables; the same tables must also be included in EN 1998-5.
Clauses 2.2 Design situations
Geotechnical design considering earthquake would better use drained and undrained conditions instead of long term and short term as in 2.2 (1) of EN 1997.
Clauses 2.4.7 Ultimate Limit States
Failure or excessive deformation of the structure induced by Liquefaction
Clauses 2.4.8 Serviceability limit states and 2.4.9 Limiting values for movements of foundations
EN 1997 and EN 1998 should provide guidance to select the limits of allowable/excessive permanent displacements both for static or seismic loading conditions.
Section 3 Geotechnical data
Guidance should be provided on:
In situ and laboratory test to assess ground behavior to cyclic-dynamic loads (consider rock discontinuities !!)
Techniques to measure the shear wave velocity with possible limitations, accuracy etc.
Laboratory tests to measure stiffness degradation and material damping, including information from well-established experience.
Clause 6.2 Limit states (for spread foundations but also for other geotechnical structures if applicable); add to the list of LS:
The occurrence of soil liquefaction under a footing or a slab (the appropriate calculation model should be presented in EN 1998)
The occurrence of excessive displacements due to the earthquake shaking.

## Slide 3
THE FOLLOWING SUGGESTIONS ARE GIVEN FOR POSSIBLE CONSIDERATION FOR EN 1998-5
Importance factors
Soil characteristics:
(§3.1 and §5.4.1.1(9)) recommendations on how to measure the shear strength of soils, rocks and filling of discon. under rapid loading and also warning on the type of material sensitive to significant cyclic degradation; should be referred to appropriate clauses of EN 1997-2 and existing standards (ref.)
(§3.2) laboratory tests to measure stiffness degradation and material damping: see EN 1997
Siting: characterization
(§3.2) suggest acceptable techniques to measure the shear wave velocity referring to EN 1997;
(§4.1.2) Geological investigations to identify active faults: the subject may be out of the scope of the Code
Design approaches and partial factors : consistent with EC7
For each adopted design approach the complete set of partial factors (model, actions, material or resistances) should be presented in appropriate tables; the same tables must also be included in EN 1997
Foundations:
Guidance on acceptable values for permanent (absolute and differential) settlements following an earthquake (5.1(1)b)
Verification for piles under lateral loading (5.4.2(2) and 5.4.2(5))
Indication of soils susceptible to significant degradation of resistance during the earthquake (nature, depth from the ground surface, etc..)
Earth retaining structures:
Table 7.1 — Values of factor r for the calculation of the horizontal seismic coefficient must be reconsidered to allow for soil permanent displacements with high seismicity
Slope stability (ASHTO tables) ductility etc..)
Capacity design and hierarchy principles (discuss the Omega factors)
Anchor system (frictional devices for energy dissipation)
Strength hierarchy principles should be introduced to ensure that anchor foundation capacity is reached before the failure of the tendons and of the restrain system.

## Slide 4
Ground type classification Part 1